## Slide 1
Autonomous Intersection Management
Ahmed Fayed & Alex Winger

## Slide 2
Project Scope & Completion
4-way 3-dedicated-lane intersection with a centralized architecture and minimum V2V communication.
No communication failure, delay, or execution error
We are using ROS and RViz for visualization.
Update:
  Visualization with RViz done
  More advanced ACC developed
  Different System modes (including our improved policy)

## Slide 3
Our Policy

## Slide 4
Challenges & Time Crunch
Developing a stress testing technique (on hold)
This will be what we added/updated:
  ACC
  RVIZ for visualization
    Not being able to use Tesla stl file
  Our policy
    Small edge cases causing failures

## Slide 5
Collision Avoidance Policy
Try trajectory with desired velocity
  Identify point of collision
  Slow down or speed up car
  Try new trajectory
  Try opposite speed
Return success or failure

## Slide 6
All Policies

## Slide 7
Have we hit our Measures of Success?
Comparing efficiency (delay) between different modes
    Traffic Lights
    Stops Signs
    Dresner & Stone’s policy
    Our policy
  Our policy should at least provide shorter delays than current Traffic Light and Stop sign systems
  Stretch goal: Shorter delay than Dresner & Stone’s policy

## Slide 8
Results
Policy | 20 cars/ 20 sec | 40 cars/ 20 sec | 60 cars/ 20 sec | 80 cars/ 20 sec | 100 cars/ 20 sec | 120 cars/ 20 sec
Ours | 0.031 | 0.068 | 0.084 | 0.206 | 0.326 | 1.957
Dresner/Stone | 0.026 | 0.057 | 0.105 | 0.575 | 0.667 | 2.898
Traffic Light | 12.078 | 11.485 | 14.336 | 24.584 | 26.250 | 25.607
Stop Sign | 10.610 | 12.849 | 15.846 | 19.062 | 22.582 | 23.050

## Slide 9
Results

## Slide 10
Results

## Slide 11
Results

## Slide 12
Extra Video with max number of cars system can handle

## Slide 13
Extra Video with Teslas (Not Accurate)